## Slide 1: Signals and Variables
Advanced Digital Electronics
Lecture 6
ALMAARIF UNIVERSITY
CET/

## Slide 2
Constant
Signal
Variable
Signal versus Variable
Number of Registers
Examples
  Outlines

## Slide 3
Introduction
VHDL provides two objects for dealing with non-static data values: SIGNAL and VARIABLE. It also provides means for establishing default (static) values: CONSTANT and GENERIC.
CONSTANT and SIGNAL:
can be global (that is, seen by the whole code), and can be used in either type of code, concurrent or sequential.
VARIABLE:
is local, for it can only be used inside a piece of sequential code (that is, in a PROCESS, FUNCTION, or PROCEDURE) and its value can never be passed out directly.

## Slide 4
CONSTANT
CONSTANT serves to establish default values. Its syntax is:
Examples:
CONSTANT set_bit : BIT := '1';
CONSTANT datamemory : memory := (('0','0','0','0'),
('0','0','0',‘1'),
('0','0',‘1',‘1'));
A CONSTANT can be declared in a PACKAGE, ENTITY, or ARCHITECTURE.

## Slide 5
When declared in a package
it is truly global, for the package can be used by several entities.
When declared in an entity
(after PORT), it is global to all architectures that follow that entity.
Finally, when declared in an architecture
(in its declarative part), it is global only to that architecture’s code.
The most common places to find a CONSTANT declaration is in an ARCHITECTURE or in a PACKAGE.
CONSTANT

## Slide 6
SIGNAL serves to pass values in and out the circuit, as well as between its internal units. In other words, a signal represents circuit interconnects (wires). For instance, all PORTS of an ENTITY are signals by default. Its syntax is the following:
Examples:
SIGNAL control: BIT := '0';
SIGNAL count: INTEGER RANGE 0 TO 100;
SIGNAL y: STD_LOGIC_VECTOR (7 DOWNTO 0);
SIGNAL

## Slide 7
The declaration of a SIGNAL can be made in the same places as the declaration of a CONSTANT (described before). A very important aspect of a SIGNAL, when used inside a section of sequential code (PROCESS, for example), is that its update is not immediate. In other words, its new value should not be expected to be ready before the conclusion of the corresponding PROCESS, FUNCTION or PROCEDURE.
Assignment operator for a SIGNAL is ‘‘<=’’ (Ex.: count<=35;).
Initial value in the syntax is not synthesizable, being only considered in simulations.
when multiple assignments are made to the same SIGNAL might infer the wrong circuit (by considering only the last assignment, for example). Therefore, a VARIABLE must be used.
SIGNAL

## Slide 8
Example 1: Count Ones #1 (not OK)
Say that we want to design a circuit that counts the number of ‘1’s in a binary vector
ENTITY count_ones IS
PORT ( din: IN STD_LOGIC_VECTOR (7 DOWNTO 0);
ones: OUT INTEGER RANGE 0 TO 8);
END count_ones;
ARCHITECTURE not_ok OF count_ones IS
SIGNAL temp: INTEGER RANGE 0 TO 8;--unnecessary ones!!!
BEGIN
PROCESS (din)
BEGIN
temp <= 0;
FOR i IN 0 TO 7 LOOP
IF (din(i)='1') THEN temp <= temp + 1;
END IF;
END LOOP;
ones <= temp;
END PROCESS;
END not_ok;

## Slide 9
Contrary to CONSTANT and SIGNAL, a VARIABLE represents only local information. It can only be used inside a PROCESS, FUNCTION, or PROCEDURE (that is, in sequential code), and its value can not be passed out directly. On the other hand, its update is immediate, so the new value can be promptly used in the next line of code.
To declare a VARIABLE, the following syntax should be used:
Examples:
VARIABLE control: BIT := '0';
VARIABLE count: INTEGER RANGE 0 TO 100;
VARIABLE y:STD_LOGIC_VECTOR(7DOWNTO0):= "10001000";
VARIABLE

## Slide 10
Since a VARIABLE can only be used in sequential code, its declaration can only be done in the declarative part of a PROCESS, FUNCTION, or PROCEDURE.
the assignment operator for a VARIABLE is ‘‘:=’’ (Ex: count:=35;).
Also, like in the case of a SIGNAL, the initial value in the syntax above is not synthesizable, being only considered in simulations.
VARIABLE

## Slide 11
Example 2: Count Ones #2 (OK)
Example 1 once again. The only difference in the solution below is that an internal VARIABLE is employed instead of a SIGNAL.
ENTITY count_ones IS
PORT ( din: IN STD_LOGIC_VECTOR (7 DOWNTO 0);
ones: OUT INTEGER RANGE 0 TO 8);
END count_ones;
ARCHITECTURE ok OF count_ones IS
BEGIN
PROCESS (din)
VARIABLE temp: INTEGER RANGE 0 TO 8;
BEGIN
temp := 0;
FOR i IN 0 TO 7 LOOP
IF (din(i)='1') THEN temp := temp + 1; END IF;
END LOOP;
ones <= temp;
END PROCESS;
END ok;

## Slide 12
-- Solution 1: using a SIGNAL (not ok) --
ENTITY mux IS
PORT ( a, b, c, d, s0, s1: IN STD_LOGIC;
y: OUT STD_LOGIC);
END mux;
ARCHITECTURE not_ok OF mux IS
SIGNAL sel : INTEGER RANGE 0 TO 3;
BEGIN
PROCESS (a, b, c, d, s0, s1)
BEGIN
sel <= 0;
IF (s0='1') THEN sel <= sel + 1; END IF;
IF (s1='1') THEN sel <= sel + 2; END IF;
CASE sel IS WHEN 0 => y<=a;
WHEN 1 => y<=b;
WHEN 2 => y<=c;
WHEN 3 => y<=d;
END CASE;
END PROCESS;
END not_ok;
Example 3: Bad versus Good Multiplexer

## Slide 13
Example 3: Bad versus Good Multiplexer
-- Solution 2: using a VARIABLE (ok) ----
ENTITY mux IS
PORT ( a, b, c, d, s0, s1: IN STD_LOGIC;
y: OUT STD_LOGIC);
END mux;
ARCHITECTURE ok OF mux IS
BEGIN
PROCESS (a, b, c, d, s0, s1)
VARIABLE sel : INTEGER RANGE 0 TO 3;
BEGIN
sel := 0;
IF (s0='1') THEN sel := sel + 1; END IF;
IF (s1='1') THEN sel := sel + 2; END IF;
CASE sel IS WHEN 0 => y<=a;
WHEN 1 => y<=b;
WHEN 2 => y<=c;
WHEN 3 => y<=d;
END CASE;
END PROCESS;
END ok;

## Slide 14
Comments:
A common mistake when using a SIGNAL is not to remember that it might require a certain amount of time to be updated. Therefore, the assignment sel <= sel‏+1 in the first solution will result in one plus whatever value had been previously propagated to sel, for the assignment sel <= 0 might not have had time to propagate yet. The same is true for sel <= sel+2. This is not a problem when using a VARIABLE, for its assignment is always immediate.
A second aspect that might be a problem in solution 1 is that more than one assignment is being made to the same SIGNAL sel, which might not be acceptable. Generally, only one assignment to a SIGNAL is allowed within a PROCESS, so the software will either consider only the last one (sel <= sel+‏ 2 in
solution 1) or simply issue an error message and stop compilation. Again, this is never a problem when using a VARIABLE.
Example 3: Bad versus Good Multiplexer

## Slide 15
A SIGNAL generates a flip-flop whenever an assignment is made at the transition of another signal; that is, when a synchronous assignment occurs. Such assignment, being synchronous, can only happen inside a PROCESS, FUNCTION, or PROCEDURE (usually following a declaration of the type ‘‘IF signal ’EVENT . . .’’ or ‘‘WAIT UNTIL . . .’’).
A VARIABLE, on the other hand, will not necessarily generate flip-flops if its value never leaves the PROCESS (or FUNCTION, or PROCEDURE). However, if a value is assigned to a variable at the transition of another signal, and such value is eventually passed to a signal (which leaves the process), then flip-flops will be inferred. A VARIABLE also generates a register when it is used before a value has been assigned to it.
Number of Registers

## Slide 16
Example:output1 and output2 will both be stored, because both are assigned at the transition of another signal (clk).
PROCESS (clk)
BEGIN
IF (clk'EVENT AND clk='1') THEN
output1 <= temp; -- output1 stored
output2 <= a; -- output2 stored END IF;
END PROCESS;
Example: output1 will be stored (output2 will make use of logic gates).
PROCESS (clk)
BEGIN
IF (clk'EVENT AND clk='1') THEN
output1 <= temp; -- output1 stored END IF;
output2 <= a; -- output2 not stored
END PROCESS;
Example: temp(a variable) will cause x(a signal) to be stored.
PROCESS (clk)
VARIABLE temp: BIT;
BEGIN
IF (clk'EVENT AND clk='1') THEN temp := a; END IF;
x <= temp; -- temp causes x to be stored
END PROCESS;
Number of Registers

## Slide 17
Example 4: DFF with q and qbar
---- Solution 1: Two DFFs ---------------
ENTITY dff IS
PORT ( d, clk: IN STD_LOGIC;
q: BUFFER STD_LOGIC;
qbar: OUT STD_LOGIC);
END dff;
------------------------------------------
ARCHITECTURE two_dff OF dff IS
BEGIN
PROCESS (clk)
BEGIN
IF (clk'EVENT AND clk='1') THEN
q <= d; -- generates a register
qbar <= NOT d; -- generates a register
END IF;
END PROCESS;
END two_dff;
21 -----------------------------------------

## Slide 18
Example 4: DFF with q and qbar
---- Solution 2: One DFF ----------------
ENTITY dff IS
PORT ( d, clk: IN STD_LOGIC;
q: BUFFER STD_LOGIC;
qbar: OUT STD_LOGIC);
END dff;
-----------------------------------------
ARCHITECTURE one_dff OF dff IS
BEGIN
PROCESS (clk)
BEGIN
IF (clk'EVENT AND clk='1') THEN
q <= d; -- generates a register
END IF;
END PROCESS;
qbar <= NOT q; -- uses logic gate (no register)
END one_dff;
-----------------------------------------

## Slide 19
Given the following VHDL objects:
CONSTANT max : INTEGER := 10;
SIGNAL x: INTEGER RANGE -10 TO 10;
SIGNAL y: BIT_VECTOR (15 DOWNTO 0);
VARIABLE z: BIT;
Determine which among the assignments below are legal
x <= 5;
x <= y(5);
z <= '1';
z := y(5);
WHILE i IN 0 TO max LOOP...
FOR i IN 0 TO x LOOP...
G1: FOR i IN 0 TO max GENERATE...
G1: FOR i IN 0 TO x GENERATE...
Home work:

## Slide 20
Questions?